## Slide 1: Deriving of threshold values in soil and groundwater for non-regulated substances
Formation risques Fedexsol

## Slide 2: Overview
1. Context
2. Objectives
3. Overall approach
  3.1 Substance properties
  3.2 Methodology – general
  3.3 Methodology – Conceptual site model
4 Derivation of threshold values based on human exposure
  4.1 Methodology
  4.2 In soil
  4.3 In groundwater
  5. Derivation of threshold values based on migration (VSN)
  6. Conclusion Arcadis
  7. Conclusion DAS

## Slide 3: 1. Context
Site contaminated with insecticides in soil and groundwater
Some contaminants are non-regulated compounds  no soil remediation standards available
Threshold values* proposed by DAS but :
  lower than or equal to the laboratory detection limit
  no threshold calculated due to absence of toxicological and/or
  physicochemical data
* Threshold values in soil and groundwater are defined as “level of contamination (in mg/kg dry matter or μg/l) above which potential negative effects on human health or the local environment cannot be excluded”
Source : https://phys.org

## Slide 4: 2. Objectives
Desk study to collect and review existing toxicological and physicochemical data on the compounds where insufficient information was identified by DAS
Use these collected data to calculate site specific threshold values for specific compounds based on Walloon methodology (GRER v2 and v3)
Notes: GRER: guide de référence pour l'étude de risques

## Slide 5: 3. Overall approach
Collection of physical-chemical and toxicological data of the non-regulated compounds if not readily available *
Development of high-level Conceptual Site Model (CSM)
Determination of the threshold values:
  based on human exposure
  based on migration (pure product and leaching to groundwater)
* Material Safety Data Sheets (MSDS), online databases (IRIS, EPA, Texas Risk Reduction Program)

## Slide 6: 3.1 Substance properties
physical-chemical data
toxicological data
MW
S
Density
VP
HLC@25°C
log Kow
Koc
Dia, Diw
Kp
If more than 1 Henry-constant  range to assess sensitivity
For compounds with lacking data  data based on surrogate compound
Tolerable daily intake (TDI) or Reference dose (Rf)
Inhalation & oral uptake

## Slide 7: 3.2 Methodology - general
Calculation of :
- VSH: threshold value in soil below which there is no risk expected to human health
- VSN: threshold value in soil below which there is no significant leaching to groundwater
- VSnappe: threshold value in groundwater below which there is no risk expected to human health
Difficult to calculate one explicit threshold value (contrasting literature data)  various threshold values based on different perspectives:
  modelling human exposure
  prevent presence of pure product (human exposure and migration)
  prevent significant leaching to groundwater (migration)
  groundwater used as drinking water
Range of threshold values  more robust understanding of anticipated risk
Notes: Contrasting H-constant referenced for some compounds

## Slide 8: 3.2 Methodology - general
Principle | Purpose
Human exposure (VSH) | The protection of human health from contamination in soil based on the model S-Risk
 | The protection of human health from the presence of pure product
Migration risks (VSN) | The protection of water resource receptors from significant leaching from soils based on VSnappe - use as drinking water
 | The protection of water resource receptors from significant leaching from soils based on VSnappe - no indication of pure product
Overview of the derived threshold values in soil
Principle | Purpose
Human exposure (VSnappe) | Protection of human health – use as drinking water
 | Protection of human health from contamination in groundwater based on the model S-Risk
 | Protection of human health from threshold values in soil (VSH)
 | Protection of human health from the presence of pure product
Overview of the derived threshold values in groundwater
Notes: S-Risk doesn’t account for pure product concentrations – actually, in case of volatile compounds, when there are indications of pure product, transport through (soil) air via diffusion is no longer applicable, but transport is driven by vapour pressure and S-Risk outcome are no longer reliable

## Slide 9: 3.3 Methodology – Conceptual site model
Site and soil characteristics :
  Industrial site  light industry
  Default characteristics and values :
    Basement with gaps and holes & drinking water pipes
    Building characteristics (volume etc)
    Generic soil layer (favours mobility of pure product)
    pH, organic content, clay content
    groundwater depth of 3 m-bgl
Light industry & default values

## Slide 10: 3.3 Methodology – Conceptual site model
Représentation schématique des voies de transfert et des voies d’exposition implémentées dans le logiciel S-Risk© (Source : S-Risk – Technical Guidance Document, VITO, 2014)
Transport routes
  light industry
  permeation trough drinking water pipe only for (mono)chlorobenzene (no other data available)
  Physical-chemical properties of compounds: high solubility and low retardation to soil  leaching to groundwater is most important transport route
Exposure routes : all but
  inhalation of bathroom air
  dermal contact through bathing/showering
  dietary intake vegetables and/or meat
Receptors
  adults
Potential / future CSM = current CSM
Notes: All possible transport routes in light industry are taken into account
Why not inhalation of bathroom air and dermal contact bath/shower? There are showers available I think

## Slide 11: 4 Derivation of threshold values based on human exposure
Principle | Purpose
Human exposure (VSH) | The protection of human health from contamination in soil based on the model S-Risk
 | The protection of human health from the presence of pure product
Migration risks (VSN) | The protection of water resource receptors from significant leaching from soils based on VSnappe - use as drinking water
 | The protection of water resource receptors from significant leaching from soils based on VSnappe - no indication of pure product
Overview of the derived threshold values in soil
Principle | Purpose
Human exposure (VSnappe) | Protection of human health from contamination in groundwater based on the model S-Risk
 | Protection of human health – use as drinking water
 | Protection of human health from threshold values in soil (VSH)
 | Protection of human health from the presence of pure product
Overview of the derived threshold values in groundwater
4.1 Derivation of threshold values based on human exposure (VSH & VSnappe) with S-Risk – Methodology
Notes: S-Risk doesn’t account for pure product concentrations – actually, in case of volatile compounds, when there are indications of pure product, transport through (soil) air via diffusion is no longer applicable, but transport is driven by vapour pressure and S-Risk outcome are no longer reliable

## Slide 12: 4 Derivation of threshold values based on human exposure
Exposure dose : Tolerable daily intake (TDI; oral, dermal and inhalation)  Risk Index (RI)
Allowable Concentrations in Air : Tolerable Concentration in Air (TCL) or legal standard  Concentration Index (CI)
Drinking water standards : legal standards  Concentration Index (CI)
Methodology
1. Determine sum of the RI (all transfer media) for the derived soil concentration. If RI > 1  adjust limit value until RI = 1
2. Determine CI per transfer medium. If CI > 1  adjust limit value until CI = 1
4.1 Derivation of threshold values based on human exposure (VSH & VSnappe) with S-Risk – Methodology
Notes: Application 3 of S-Risk calculates soil (or groundwater)concentrations at which the criteria are met (per trasfermedium RI=1, sum of RI = 1, ExCR = 1 and CI = 1 per medium)

## Slide 13: 4.2 Derivation of threshold values based on human exposure (VSH) in soil – Prevention of pure product
Principle | Purpose
Human exposure (VSH) | The protection of human health from contamination in soil based on the model S-Risk
 | The protection of human health from the presence of pure product
Migration risks (VSN) | The protection of water resource receptors from significant leaching from soils based on VSnappe - use as drinking water
 | The protection of water resource receptors from significant leaching from soils based on VSnappe - no indication of pure product
Overview of the derived threshold values in soil
Principle | Purpose
Human exposure (VSnappe) | Protection of human health from contamination in groundwater based on the model S-Risk
 | Protection of human health – use as drinking water
 | Protection of human health from threshold values in soil (VSH)
 | Protection of human health from the presence of pure product
Overview of the derived threshold values in groundwater
Notes: S-Risk doesn’t account for pure product concentrations – actually, in case of volatile compounds, when there are indications of pure product, transport through (soil) air via diffusion is no longer applicable, but transport is driven by vapour pressure and S-Risk outcome are no longer reliable

## Slide 14: 4.2 Derivation of threshold values based on human exposure (VSH) in soil – Prevention of pure product
Pure product = potential risk to human health
S (mg/l): maximum solubility (substance specific)
Kd (l/kg): soil water partitioning coefficient (substance specific)
Koc (l/kg): organic carbon – water partition coefficient (substance specific)
foc (-): fraction organic carbon, foc = OM x 0.0058
OM (%): organic matter (default value = 1.6 %)
Contaminant concentration in soil < 10 % max solubility  pure product not expected
Source: Advances in remediation, a new way of thinking. Arcadis, 2016

## Slide 15: 4.2 Derivation of threshold values based on human exposure (VSH) in soil – Comparison
2 values for allowable concentration in soil :
  based on S-Risk model
  based on pure product prevention
  Most stringent value = lower limit for human toxicological threshold value
  Highest value = upper limit
Range of threshold values
Principle | Purpose
Human exposure (VSH) | The protection of human health from contamination in soil based on the model S-Risk
 | The protection of human health from the presence of pure product

## Slide 16: 4.2 Derivation of threshold values based on human exposure (VSH) in soil
Until 3 orders of magnitude difference S-Risk & Solubility
Note : different H-constants for some compounds did not effect the calculated human
toxicological threshold value in soil
Parameter |  | VSH (mg/kg) Calculated with S-Risk | Theoretically calculated value corresponding to 10% solubility * (mg/kg)
Acetochlor |  | 122 10³ | 62
Diallate |  | 3 | 8
Dicamba |  | 248 10³ | 224
Diquat |  | 13 10³ | 6 106
Glyphosate |  | 1 106 | 14 10³
(mono)chlorobenzene |  | 25 | 0.9
Napropamide |  | 597 10³ | 218
Paraquat |  | 27 10³ | 5 106
Propionic acid |  | 1 106 | 1250
Thiocarbamates | Butylate | 303 10³ | 16
 | Cycloate | 338 10³ | 19
 | S-ethyl dipropylthiocarbamate (EPTC) | 153 10³ | 57
 | Esprocarb | 30 10³ | 20
 | Ethiolate | 3 | 164
 | Molinate | 8969 | 164
 | Orbencarb | 30 10³ | 8
 | Pebulate | 296 10³ | 28
 | Prosulfocarb | 30 10³ | 233
 | Vernolate | 4716 | 25
(1) Concentration in the soil corresponding to 10% maximum solubility in the groundwater (converted via the Kd)

## Slide 17: 4.3 Derivation of threshold values based on human exposure (VSnappe) – Calculation in groundwater
Principle | Purpose
Human exposure (VSH) | The protection of human health from contamination in soil based on the model S-Risk
 | The protection of human health from the presence of pure product
Migration risks (VSN) | The protection of water resource receptors from significant leaching from soils based on VSnappe - use as drinking water
 | The protection of water resource receptors from significant leaching from soils based on VSnappe - no indication of pure product
Overview of the derived threshold values in soil
Principle | Purpose
Human exposure (VSnappe) | Protection of human health from contamination in groundwater based on the model S-Risk
 | Protection of human health – use as drinking water
 | Protection of human health from threshold values in soil (VSH)
 | Protection of human health from the presence of pure product
Overview of the derived threshold values in groundwater
Notes: S-Risk doesn’t account for pure product concentrations – actually, in case of volatile compounds, when there are indications of pure product, transport through (soil) air via diffusion is no longer applicable, but transport is driven by vapour pressure and S-Risk outcome are no longer reliable

## Slide 18: 4.3 Derivation of threshold values based on human exposure (VSnappe) – Calculation in groundwater
Threshold value via model calculations : S-Risk
Threshold value for use as drinking water
Non-carcinogenic substances Carcinogenic substances
RfD0: Oral Reference dose (mg/kg bw.d) SF: slope factor ((mg/kg bw.d)-1)
W: body weight (60 kg)
Q: drinking water consumption per person (2 l/d)
RF: reduction factor : contribution of the general exposure of the
population to the substance, (default value = 0,2)

## Slide 19: 4.3 Derivation of threshold values based on human exposure (VSnappe) – Calculation in groundwater
Threshold value based on VSH and no pure product
Fv (-) : redistribution factor in the unsaturated zone (default value = 1)
Ksw (kg/l) :soil water partitioning factor
FD : dilution factor (default value = 30)
Range of threshold values

## Slide 20: 4.3 Derivation of threshold values based on human exposure (VSnappe) in groundwater – Comparison
4 values for allowable concentration in groundwater :
  based on S-Risk model
  for use as drinking water
  based on VSH
  based on no pure product
  Calculated threshold values based on the use of drinking water = lower limit for human toxicological threshold value
  Most stringent of VSnappe,H with S-Risk and VSnappe,10% S = upper limit
Range of threshold values
Principle | Purpose
Human exposure (VSnappe) | Protection of human health from contamination in groundwater based on the model S-Risk
 | Protection of human health – use as drinking water
 | Protection of human health from threshold values in soil (VSH)
 | Protection of human health from the presence of pure product

## Slide 21: 4.3 Derivation of threshold values based on human exposure (VSnappe) in groundwater – Comparison
Until 3 orders of magnitude difference S-Risk & Solubility
Parameter |  | VSnappe (µg/l) | VSnappe, H (µg/l) with S-Risk | VSnappe, VSH (µg/l) with S-Risk | VSnappe, 10%S (µg/l)
Acetochlor |  | 120 | Max. solubility | 2 106 | 923
Diallate |  | 5* | 600 | 22 | 60
Dicamba |  | 180 | Max. solubility | 23 106 | 21 10³
Diquat |  | 13.2 | Max. solubility | 6751 | 3 106
Glyphosate |  | 600 | Max. solubility | 5 106 | 63 10³
(mono)chlorobenzene |  | 120 | 13 10³ | 4474 | 166
Napropamide |  | 600 | Max. solubility | 883 10³ | 322
Paraquat |  | 27 | Max. solubility | 14 10³ | 3 106
Propionic acid |  | 3 10³ | Max. solubility | 206 106 | 257 10³
Thiocarbamates | Butylate | 300 | Max. solubility | 164 10³ | 9
 | Cycloate | 330 | Max. solubility | 5 106 | 308
 | S-ethyl dipropylthiocarbamate (EPTC) | 150 | Max. solubility | 4 106 | 1470
 | Esprocarb | 30 | Max. solubility | 33 10³ | 22
 | Ethiolate | 5* | 2700 | 70 | 3848
 | Molinate | 12 | Max. solubility | 211 10³ | 3848
 | Orbencarb | 30 | Max. solubility | 217 10³ | 60
 | Pebulate | 300 | Max. solubility | 4 106 | 414
 | Prosulfocarb | 30 | Max. solubility | 7490 | 59
 | Vernolate | 6 | Max. solubility | 211 10³ | 373
* Threshold value calculated according to the formula for carcinogenic substances
Note : different H-constants for some compounds did not effect the calculated human
toxicological threshold value in groundwater

## Slide 22: 5. Derivation of threshold values based on migration (VSN)
Potential leaching of contaminants from soil to groundwater  risk to water resource receptors
Source: Code de Bonnes pratiques pour l’étude de risques. Bruxelles Environnement, v 31/05/2019
Principle | Purpose
Migration risks (VSN) | The protection of water resource receptors from significant leaching from soils based on VSnappe - use as drinking water
 | The protection of water resource receptors from significant leaching from soils based on VSnappe - no indication of pure product

## Slide 23: 5.1 Derivation of threshold values based on migration (VSN) - methodology
VSnappe (μg/l): threshold value in groundwater (substance specific)
FD: dilution factor (default value = 30)
Fv (-): redistribution factor in the unsaturated zone (default value = 1)
Ksw (kg/l), the soil water partitioning factor
Notes: VSnappe = concentration for use as drinking water
Also instead of Vsnappe, 10% solubility used for prevention of pure product

## Slide 24: 5.1 Derivation of threshold values based on migration (VSN) - methodology
fads: adsorption factor (default value for industry = 0.75)
Kd (l/kg): soil water partitioning coefficient (substance specific)
ρb: soil density (default value = 1.45 kg/dm³)
H’: dimensionless Henry constant (substance specific)
θv: water filled porosity
θg: air filled porosity
f: fraction of the pores filled with water (default value = 0.5)

## Slide 25: 5.2 Derivation of threshold values based on migration (VSN) – Comparison
2 values for allowable concentration in soil :
  Based on conservative groundwater concentration (drinking water quality)
  Based on a groundwater concentration that equates to 10% solubility (prevention of pure product)
  Most stringent of VSN and VSN,10% S = lower limit
  Hihest value = upper limit
Range of threshold values
Principle | Purpose
Migration risks (VSN) | The protection of water resource receptors from significant leaching from soils based on VSnappe - use as drinking water
 | The protection of water resource receptors from significant leaching from soils based on VSnappe - no indication of pure product

## Slide 26: 5.2 Derivation of threshold values based on migration (VSN) – Comparison
Until 6 orders of magnitude difference
Parameter |  | VSN (mg/kg) | VSN, 10%S (mg/kg)
Acetochlor |  | 8 | 1491
Diallate |  | 0.7 | 195
Dicamba |  | 2 | 8836
Diquat |  | 26 | 137 106
Glyphosate |  | 128 | 312 10³
(mono)chlorobenzene |  | 0.7 | 279
Napropamide |  | 406 | 4938
Paraquat |  | 52 | 486 106
Propionic acid |  | 14.5 | 486 10³
Thiocarbamates | Butylate | 25 | 383
 | Cycloate | 20 | 460
 | S-ethyl dipropylthiocarbamate (EPTC) | 6 | 1457
 | Esprocarb | 27 | 448
 | Ethiolate | 0.2 | 4128
 | Molinate | 0.5 | 4128
 | Orbencarb | 4 | 195
 | Pebulate | 20 | 671
 | Prosulfocarb | 119 | 5250
 | Vernolate | 0.4 | 603
Note : different H-constants for some compounds did not effect the calculated threshold leaching value, except for butylate

## Slide 27: 6 Conclusion Arcadis
Proposed threshold values for soil based on both human health risks and significant leaching to groundwater
Proposed threshold values for groundwater based on both human health risks, migration risks and use as drinking water
Proposed value by Arcadis
If value DAS in range value Arcadis  value DAS proposed
If value DAS higher than value Arcadis  value DAS proposed
If value DAS lower than value Arcadis  lower limit Arcadis proposed
Compounds with detection limits (DL) higher then proposed threshold values => 5 x DL
Threshold values DAS much lower than threshold values Arcadis  new propositions

## Slide 28: 7 Conclusion DAS
DAS partially agreed on threshold values proposed by Arcadis
Did DAS agree with the proposed threshold values? …
Notes: The proposed threshold values by Arcadis in soil based on human exposure which were higher than the DAS-values were not accepted, but the higher threshold values to prevent leaching we proposed in soil were accepted.
We certainly did not do unnecessary work by calculating groundwater threshold values => these will still be considered when remediation needs to be done